## Slide 1: DSM2 Sediment Transport Module
DSM2 User Group and CWEMF sponsored
Technical Advisory Committee Meeting
January 13, 2010
Jamie Anderson, Ph.D., P.E.
Department of Water Resources
Modeling Support Branch
Bay-Delta Office

## Slide 2: Thanks to CWEMF for the refreshments
California Water and Environmental Modeling Forum
cwemf.org

## Slide 3: Agenda
Welcome and Introductions
Questionnaire
Project Overview Jamie Anderson, DWR
Project Progress Jamie Anderson, DWR and Fabian Bombardelli, UCD
Issues for TAC Input Fabian Bombardelli, UCD
Discussion and wrap up
Web site for materials:
http://baydeltaoffice.water.ca.gov/modeling/deltamodeling/models/stm/stm.cfm

## Slide 4
Name
Affiliation
Interest / experience with sediment transport

## Slide 5: Issues Related to Sediment Transport in the Delta
Dredging
Levee failures
Marsh restoration
Turbidity / fish migration
Mercury/heavy metal transport
Channel bed level changes
  Erosion
  Deposition

## Slide 6: Contract to Develop STM
2 year MACHRO contract with UC Davis
PI Fabian Bombardelli Civil & Env. Engineering
  Graduate student Kaveh Zamani (modeling)
  Graduate students Jamie Kohne & Joseph Waltz (data)*
Project products
  Web site with available sediment data in the Delta
  Sediment Transport Module (STM) for DSM2
    Suspended sediment and bed load
    Multiple sediment class sizes
    One-dimensional model
*supported by another funding source
STM=Sediment Transport Module

## Slide 7: DSM2 Sediment Transport Module
PTM
Particle Tracking
QUAL
Water Quality
STM
Sediment Transport
HYDRO
Hydrodynamics

## Slide 8: STM Project Deliverables
Establish Technical Advisory Committee
  Meet twice a year
1-D sediment transport code-STM
Website with available Delta sediment data
Documentation
  Progress reports
  Complete code documentation and user manual
  Journal articles
Training on how to use STM
STM=Sediment Transport Module

## Slide 9: STM Code Development Plan
Flexible, modular design
Separate input/output routines to aid in generalization to other codes
Generalize Eulerian transport that could be adapted to other constituents
STM=Sediment Transport Module Eulerian=fixed frame of reference

## Slide 10: Why did we create a new transport code instead of using QUAL?
QUAL is a moving frame of reference (Lagrangian) model
STM is a fixed frame of reference (Eulerian) model
  Compatibility with other Eulerian codes
  Clean slate, develop testable code
  Separate sources from transport
    Sediment is one of the sources, but model could be applied to other sources as well
  Sharing resources with a companion project
  Future benefits
    Could incorporate baroclinic term from HYDRO
    Could be used for salinity based operating rules

## Slide 11: STM Code Development Plan
Flexible, modular design
Separate input/output routines to aid in generalization to other codes
Generalize Eulerian transport that could be adapted to other constituents
Self-documenting code using Doxygen
STM=Sediment Transport Module Eulerian=fixed frame of reference

## Slide 12: Self-Documenting Code using Doxygen

## Slide 13: Self-Documenting Code using Doxygen

## Slide 14: Self-Documenting Code using Doxygen

## Slide 15: STM Code Development Plan
Flexible, modular design
Separate input/output routines to aid in generalization to other codes
Generalize Eulerian transport that could be adapted to other constituents
Self-documenting code using Doxygen
Companion testing routines
STM=Sediment Transport Module Eulerian=fixed frame of reference

## Slide 16: STM Code Testing
STM=Sediment Transport Module
STM Code
Testing Code
Calls STM Code
Each routine in STM has companion testing code
Code and analytical tests
Test wide range of scenarios
Produce report of pass/fail result for all tests
Run tests regularly, in future automatic daily running of tests

## Slide 17: Fortran Unit Test Framework (FRUIT)
Unit testing
  a software verification and validation method in which a programmer tests if individual units of source code
FRUIT
  open source
  written in Fortran 95
  has assertion (true/false pass/fail), fixture, setup, teardown, report, spec generation, driver generation

## Slide 18: Sample Code Test: Gradient
Code test
  gradient
Add content

## Slide 19: Analytical Test: Diffusion of one unit of mass
Symmetrical C=1/∆X at X=0 c=0 everywhere else

## Slide 20: Analytical Test: Diffusion
Neumann boundary condition at x=0.1 (specify slope)
Dirichlet boundary condition at x=1.0 (specify value)
Concentration
Distance from 0.1 to 1
Exact solution
Numerical solution at
various times

## Slide 21: STM Code Development Plan
Flexible, modular design
Generalize Eulerian transport that could be adapted to other constituents
Self-documenting code using Doxygen
Companion testing routines
Assistance with code development by DWR staff
  lead by Kevin Kao additional input Eli Ateljevich and Nicky Sandhu
  version control
Training on use of the model
STM=Sediment Transport Module Eulerian=fixed frame of reference

## Slide 22: Sediment Transport Processes
Advection
Go with the flow
Advection
Dispersion
Erosion
Deposition
Source/Sink
Tributaries
Erosion /
Entrainment
+ and –
Sources and Sinks
Dispersion
Spreading out
Deposition/
Settling
Progress to Date: Single Channel
Advection
Dispersion
Erosion
Advection
Dispersion
Erosion
Deposition
Source/Sink
Tributaries
Next step: Complete single channel model
Next step: Extend model to a channel network

## Slide 23: Highlights from TAC July 2009
Add content

## Slide 24: Available Field Data
Compiled by Jamie Kohne and Joseph Waltz at UCD
Report and links will be posted on the web
What data do we need?
What data are available?
How do we deal with any data deficiencies?

## Slide 25
Technical
Details

## Slide 26: California Water and Environmental Modeling Forum Conference
Feb 22-24, 2010
Asilomar near Monterey
STM update in DSM2 session
cwemf.org

## Slide 27
Thank You!
Jamie Anderson
jamiea@water.ca.gov 916-654-5455
Fabian Bombardelli
fabianbombardelli2@gmail.com
530-752-0949
Photo by Ralph Finch Jan 4, 2006

## Slide 28
Extra Slides

## Slide 29: Delta Grid shaded by Manning’s n
Value range
0.018 (dark blue) to
0.045 (pink)
DSM2 Mini-calibration Grid

## Slide 30: Modes of Application
Historical
Replicate historical conditions
Forecasting
(Real-Time)
Project conditions for the near future
Planning
Hypothetical Delta changes
DSM2
Modes of Application

## Slide 31: Delta Simulation Model 2 Domain
Bay-Delta detail image from CALFED
San
Francisco
San Diego
Redding
Los Angeles
Sacramento
Stockton
San
Francisco
Sacramento
River
San
Joaquin
River
DSM2 Domain
HYDRO-flow and velocity
QUAL-water quality
PTM-particle tracking

## Slide 32: DSM2 Boundary Conditions
Grid Image from USBR GIS Group
Sacramento
Stockton
Exports
Sacramento
River
San Joaquin River
Tidal Stage or Concentration
Tributaries
Martinez
San Joaquin River
Inflow or concentration
Withdrawals
Consumptive Use

## Slide 33: Hydro
Unsteady, one-dimensional, open channel flow model
Uses four-point-implicit solution scheme
Engine Developed by Lew DeLong (USGS). Module for Delta Developed by DWR Staff
Input Required
  Delta geometry
  Mannings n (calibration parameter)
  Gate operation
  Boundary Flows – inflows, exports, diversions
  Boundary Stage (currently at Martinez)
  Initial Conditions
  Time step (usually 15 minutes)
  Output Type and Locations
Notes: NAME
FourPt - An unsteady, one-dimensional, open-channel flow model
ABSTRACT
FOURPT is a numerical model for simulating unsteady, one-dimensional
flow in networks of open channels. Options particularly useful in
training or prototyping include selection of governing equations
(kinematic, diffusion, or dynamic), boundary-value perturbation, and
user-programmable constraint equations. The model can simulate non-
trivial concepts, such as flow in complex interconnected channel
networks, meandering channels with variable effective flow lengths,
hydraulic structures defined by unique three-parameter relations,
and density-driven flow. Channel geometry may be rectangular,
trapezoidal, or irregular depending upon which of three channel-
property modules is linked with the program.
METHOD
As implied by the name, FOURPT uses the four-point-implicit solution
scheme. Simultaneous equations are solved by Gaussian elimination
using an indexed, asymmetric, sparse-matrix solver that is
particularly useful in application to large (hundreds of channels),
complex networks of interconnected channels. All relations
constraining unknown variables, discharge and water-surface
elevation, at boundaries and channel junctions are implemented
implicitly. The model is coded in Fortran 77, and data
encapsulation is used extensively to simplify modification and to
encourage the modification and use of FOURPT modules by other
programs and programmers.

## Slide 34: Qual
Branched Lagrangian Transport Model
Engine Developed by Harvey Jobson (USGS), Qual Module developed by DWR Staff
Models dispersion of conservative constituents
Models kinetics and dispersion of non conservative constituents
Input
  Delta geometry
  Dispersion Coefficients (calibration parameter)
  Rate Coefficients (calibration parameter for Non conservative coefficient)
  Gate operation
  Velocities and flow areas from Hydro output (Tide File)
  Inflow and Ocean Boundary Quality
  Atmospheric Inputs if needed for non conservative constituent modeling
  Boundary Stage (currently at Martinez)
  Initial Conditions
  Time step (usually 15 minutes)
  Output Type and Locations

## Slide 35: Model Dimensionality
Characteristics
Averaged
Characteristics
Averaged
Characteristics
Averaged
a) 1-D representation
b) 2-D depth-averaged representation
c) 2-D laterally-averaged representation
d) 3-D representation
DSM2

## Slide 36: STM Project Tasks
Task 1: Development of a sediment transport module for DSM2 able to deal with cohesive and non-cohesive sediment.
Task 2: Verification and validation of STM with laboratory tests taken from the literature.
Task 3: Organization of an inventory of datasets with information on sediment transport in the Delta.
Task 4: Selection of scenarios from datasets corresponding to sediment transport in the Delta, and validation of the sediment transport module with those scenarios.
Task 5: Application of the resulting numerical model to assess historical and future conditions in the Delta
STM=Sediment Transport Module

## Slide 37: Sediment Data Sources
Suspended Sediment
  USGS
    continuous monitoring 1989-2007
    Quarterly reports for water year 1998
Total Suspended Solids
  Bay and Delta Tributaries Project
  Sacramento Regional County Sanitation District (6xyr)
Turbidity
  USGS real time water quality monitoring
  Bay and Delta Tributaries Project (BDAT)
  Sacramento Regional County Sanitation District (6xyr)
  IEP 15 min for year 2000
  Sacramento Municipal Utility District (SMUD) seasonal
Bathymetry
  DWR Central District (twice per year), Division of Engineering
Particle Size Distribution
  Ted Swift, DWR 6 distributions from throughout the Delta