## Slide 1: Using Software Quality and Algorithm Testing to Verify a 1-Dimensional Transport Model
World Environmental and Water Resources Congress
Palm Springs, May 23, 2011
Kaveh Zamani
Fabian Bombardelli
Eli Ateljevich
Jamie Anderson
Modeling Support Branch, Bay-Delta Office
Department of Water Resources
Civil & Environmental Engineering Dept.
University of California, Davis

## Slide 2: Verification: how to find a bug in a forest?

## Slide 3
There were 8/12 serious static faults per 1000 lines of executable files in C/Fortran! (SAND 2002-0529)

## Slide 4: How to develop a fully testable and tested transport code?
This Talk:
STM (Sediment and Transport Module)
Software testing
Verification measures
Transport test suite
Challenges
Result

## Slide 5: STM:Software testing: Verification:Transport test: Challenges:Results : Governing Equation and Solution Algorithm
Operator splitting to combine:
Modified Lax Two Step method + ODE integrator (Advection, Reaction )
Crank- Nicolson in FVM framework (Dispersion)
HYDRO
Hydrodynamic
QUAL
1-D fate and transport
PTM
Quasi 3-D particle Tracking
Structure of Delta Simulation Model 2 (DSM2)
STM
1-D sediment transport model

## Slide 6: STM:Software testing: Verification:Transport test: Challenges:Results : STM Project Goals
Modular design
Applicable in tidal environments
Generalize Eulerian transport solver that could be adapted to other constituents
Second order accuracy
Shock capturing
Mass conservative
Well tested
Associated dynamic testing for development

## Slide 7: STM:Software testing: Verification:Transport test: Challenges:Results : STM Code Testing
STM=Sediment and Transport Module
Each function in STM has tests
Code and analytical tests
Each test puts light of a part
Test wide range of scenarios
Test for bad/incomplete input
Produce report of pass/fail result
Run tests regularly
(Fortran Unit Test Framework)

## Slide 8: STM:Software testing: Verification:Transport test: Challenges:Results : Convergence
Testing versus analytical solution
Richardson Extrapolation
Method of Manufactured Solution
Prescribed Forcing Method
Perturbation
Using symmetry
Error analysis
Dense mesh solution

## Slide 9
No! They are brutal. They expose bugs. But they leave behind some bugs as well.
Grid Size
Error
1
Nominal scheme’s order of accuracy (2)
1
1
A
B
a
b
2≈a > b
After Leveque, 2002
STM:Software testing: Verification:Transport test: Challenges:Results :
Are convergence tests enough?

## Slide 10
Adapted from Oberkampf and Trucano, 2002
STM:Software testing: Verification:Transport test: Challenges:Results :
Transport Test Suite

## Slide 11
Boundary values: remote Active
Flow field and coefficients: constant Variable
Single process Double process Triple process
2nd order
accuracy
STM:Software testing: Verification:Transport test: Challenges:Results :
Incremental nature of the tests

## Slide 12
STM:Software testing: Verification:Transport test: Challenges:Results :
Layering in complexity

## Slide 13
STM:Software testing: Verification:Transport test: Challenges:Results :
Layering in complexity

## Slide 14
STM:Software testing: Verification:Transport test: Challenges:Results :
Layering in complexity

## Slide 15
STM:Software testing: Verification:Transport test: Challenges:Results :
Layering in complexity

## Slide 16
STM:Software testing: Verification:Transport test: Challenges:Results :
Layering in complexity

## Slide 17
Considering error distribution
Dimensionless numbers of natural phenomena
Preserving the basic shape
Oscillation
Smoothness of initial condition
Non-linear/stiff source term
Grid Size
Error
Machine precision
exceeds round off error
Computer
precision
1
Order of Converge
III
II
I
STM:Software testing: Verification:Transport test: Challenges:Results :
General consideration

## Slide 18
Chart: Channel Length (0 to L)









STM:Software testing: Verification:Transport test: Challenges:Results :
Logical error in Advection-Reaction

## Slide 19
In boundary cells, local reduction up to 2 order does not reduce the global convergence rate.
Inside the domain cells, local reduction up to 1 order does not reduce global convergence rate.
✔
STM:Software testing: Verification:Transport test: Challenges:Results :
Syntax error in Diffusion

## Slide 20
Chart: Channel Length (m)
STM:Software testing: Verification:Transport test: Challenges:Results :
Example Advection Reaction, Tidal Flow

## Slide 21
We developed a step by step roadmap for complete verification of a transport code
Approximately 350 tests - 280 unit tests and 70 system/algorithm tests are there.
We designed a really complete test suite
  May help solve the “grey literature” issue in testing transport
  Methods of Computer Science are there to guarantee the results in computational fluid mechanics
STM is, an open source, well tested, and nice bedrock for further development
STM:Software testing: Verification:Transport test: Challenges:Results :
Accomplishments and final remarks
Notes: Competition between code users and writers on one side and experimentalist prevents collaboration

## Slide 22: Thank You
Analog Delta Model
Kaveh Zamani: kzamani@ucdavis.edu
Fabian Bombardelli, PhD: fabombardelli@ucdavis.edu
Eli Ateljevich, PhD, PE: eli@water.ca.gov
Jamie Anderson, PhD, PE: jamiea@water.ca.gov